## Slide 1
CNN inference on 2-D Systolic Array
Clocked Out
Ahmet Emre Eser, Ashita Singh, Devansh Gupta, Riyansh Chaturvedi, Rohan Nafde, Shoumik Panandikar
Motivation
2D Systolic Array
VGGNet With Quantization Aware Training
Mapping on FPGA (Cyclone IV GX)
This project develops three specialized 2-D systolic array variants: a weight stationary design for efficient data reuse, a SIMD version supporting 2-bit and 4-bit operations, and a hybrid architecture with configurable weight and output stationary modes. Performance optimizations and comprehensive testing ensure robust acceleration across diverse neural network workloads.
 | VGGNet 16 (4 bit) | VGGNet 16 (2 bit)
Accuracy (CIFAR 10) | 89.560% | 85.360%
 | VGGNet 16
Total OPs | 128
Frequency | 130.34 MHz
TOPs | 0.01668
Dynamic Power | 31.24 mW
TOPs/W | 0.534
Total Logic Elements | 22,556
Total Registers | 12,146
Alpha 1: Simultaneous Accumulation
Alpha 3: Unified Memory
Alpha 2: Functional Verification
Base Versions
Vanilla (Weight Stationary):The baseline architecture implements the fundamental Weight Stationary (WS) dataflow, primarily optimizing for weight reuse efficiency.
SIMD Enhanced (2/4-bit Precision): Features a Single Instruction, Multiple Data (SIMD) data path to support 2-bit and 4-bit input precision, increasing throughput for quantized neural network operations.
Unified Stationary (WS & OS): Implements a flexible structure supporting dynamic switching between Weight Stationary (WS) and Output Stationary (OS) dataflows, aiming for applicability across various computation patterns.
Concept: To ensure the integrity of our systolic array, we employ a rigorous hardware-software verification methodology.
Implementation: We utilize random stimulus testing where the array is fed random numerical inputs (weights and feature maps) spanning the full supported bit precision. A Golden Reference Model concurrently calculates the expected output. The hardware result is then compared against the Golden Result to confirm functional correctness across all operational modes.
Concept: In Output Stationary mode, the Partial Sum Memory (pmem) is bandwidth-heavy during accumulation but often idle during the initial weight loading phase.
Optimization: We reuse the existing high-bandwidth pmem (128-bit) to store weights instead of adding a separate, dedicated Kernel Memory (kmem).
Benefit: This removes the need for an additional 32-bit SRAM bank entirely. Since SRAM blocks dominate the silicon area of a core, eliminating one significantly reduces the total hardware footprint and static power leakage.
Alpha 4: Circuit Level Power Optimizations
Data Gating: When either the weight or activation is zero, the output simplifies to psum, making the MAC computation unnecessary. The MAC unit is bypassed using a MUX that forwards the psum to the output, while all inputs to the MAC are forced to zero. This prevents unnecessary switching activity within the MAC unit, saving dynamic power
Clock gating: Weight and load enable registers hold their values stable for long periods. When a register's load enable is inactive, clock gating prevents the flip-flops from toggling, avoiding the charging and discharging of internal capacitances, hence saving dynamic power.
Data gating circuit
Clock gating circuit
We've implemented in-place accumulation through the SFP pipeline. Each SFP lane holds a dedicated accumulator register that stores the running sum of partial psums (kij) from the MAC array via OFIFO, accumulating them internally
Only the final 8×8 block psum is written to SRAM, reducing memory traffic and eliminating intermediate writes. This achieves in-place accumulation within the hardware pipeline.